## Slide 1: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 2: TCP: Overview RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size

## Slide 3: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 4: TCP seq. numbers, ACKs
sequence numbers:
  byte stream “number” of first byte in segment’s data
acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender

## Slide 5: TCP seq. numbers, ACKs
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
simple telnet scenario
Host B
Host A
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80

## Slide 6: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 7: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 8: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
estimate SampleRTT deviation from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 9: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 10: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
  pipelined segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
let’s initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 11: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments

## Slide 12: TCP sender (simplified)
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., “send”)
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above
retransmit not-yet-acked segment with smallest seq. #
start timer
timeout
if (y > SendBase) {
SendBase = y
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK field value y

## Slide 13: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
premature timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92

## Slide 14: TCP: retransmission scenarios
X
cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120

## Slide 15: TCP ACK generation [RFC 1122, RFC 2581]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap

## Slide 16: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs.
if sender receives 3 ACKs for same data
(“triple duplicate ACKs”), resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
(“triple duplicate ACKs”),

## Slide 17: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 18: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 19: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may
remove data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 20: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow
receiver-side buffering

## Slide 21: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 22: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 23: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 24: Agreeing to establish a connection
2-way handshake failure scenarios:
retransmit
req_conn(x)
ESTAB
req_conn(x)
half open connection!
(no client!)
client terminates
server
forgets x
connection
x completes
retransmit
req_conn(x)
ESTAB
req_conn(x)
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x

## Slide 25: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN

## Slide 26: TCP 3-way handshake: FSM
closed
L
listen
SYN
rcvd
SYN
sent
ESTAB
Socket clientSocket =
newSocket("hostname","port number");
SYN(seq=x)
Socket connectionSocket = welcomeSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1)
create new socket for
communication back to client
SYNACK(seq=y,ACKnum=x+1)
ACK(ACKnum=y+1)
ACK(ACKnum=y+1)
L

## Slide 27: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 28: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB